## Slide 1: E2E Exposure Data Processing
Ricardo Piedrahita
6/3/2019

## Slide 2: Overview
Data organization
Data analysis approach
Dataset outputs for further analyses
R codes needed for generating the required data sets
Input data needed for R analyses

## Slide 3: Data organization
Dropbox
  Field sheets
    Emissions – entered from paper into Excel sheet
    Weekly instrument checks/maintenance - Excel sheet
  Surveys (from Mobenzi Researcher)
  Calibrations (in
  Household Instrument Data (one folder for each home’s deployment)
    MicroPEM data (RTI/Liverpool)
    PATS+ data
    Emissions files (UPAS and TSI)
    LASCAR CO
    Beacon Logger Data
    Ambient air pollution data (UPAS, PATS+, Lascar)

## Slide 4: Data analysis approach
QA/QC
  Individual data import functions by instrument/survey
  Individual data flagging functions
    Including file name checking
  Batch scripts for automated processing/emails
Final datasets: for each data stream
  Apply import and apply flagging function
  Apply calibration data or filter weight correction factor by logger ID and sample ID
Modeling code
  Markdown - Import all final data sets

## Slide 5: Data streams
Database Name (long) | Input files | Information | ID level | Database name (short); Processing Script
(1) Household surveys | Rapid Survey; In-depth survey; Pre-placement survey; post placement survey | Household demographic, SES, WASH, PW health care cost, income, cooking time, cookstove cost, self-reported cooking behavior, cookstove type, other source of exposure | HHID | Household_BL; Not yet written
(2) Household air pollution | Beacon Logger Lascar PATS+ | Kitchen and outdoor CO and PM2.5 (gravimetric-corrected realtime) | HHID; LocationID | Household_air_pollution; Household_air_pollution.R exists, but must be adapted
(3) Personal PM exposure | MicroPEM data; ECM | personal ECM/pump install, start log, end log, in-field QC, wear compliance | HHID, LocationID, DeviceID | Area_PM_exp; Area_PM_exp_processing exists, but must be adapted.
(4) Personal CO data | Lascar data; CO Calibration sheet |  | HHID, LocationID, DeviceID | CO_exp; CO_exposure.R exists but must be adapted.
(5) Beacon Data | Beacon Logger Data | Can adapt from the Shiny code to perform this analysis, or use the Matlab version. | HHID, LocationID, DeviceID | Beacon_exp
(6) Emissions | Emissions field sheet; UPAS; TSI | CO, CO2, fuel used, food cooked, time cooking, cooking type. CO decay to estimate ventilation rate. | HHID, LocationID, DeviceID | 
(7) Instrument IDs | Equipment List |  |  | 
(8) SUMs Data | Geocene SUMs results | Cooking events | HHID, StoveType, LocationID | 
(10) Ambient data | UPAS; PATS+; Lascar | Weekly ambient samples |  | 
(9) Joined database | All of the above | Minute data or 5 minute data? Depends on the MicroPEM settings | HHID, StoveType, LocationID, DeviceID | 
Bold = imported

## Slide 6: UPAS Specific Overview
QA/QC
  Import function UPAS data
  Flagging function
    Check flow rate, shutdown reason, pressure, temperature
  Filename checking function (of the study ID)
  Automated processing/emails
Final datasets
  Apply import and apply flagging function
  Apply calibration data or filter weight correction factor by logger ID and sample ID

## Slide 7: Code workflow for UPAS deployment data stream
Imports data from Dropbox, analyzes them, sends summary
Later combined with grav results
Code name | Inputs | Outputs | Notes
Thresholds.R | -- | Threshold values used for generating flags | See readme for details
Functions.R | Data files | Summary of data; upas_summary.R | 
localBatchScript.R | Data files; thresholds.R; functions.R | CSV file with summary of UPAS results and flags | 
HAPIN_quack.R | All above files; | CSV file with file summaries, sent to selected IRC recipients. Then used in the QAQC Excel doc | 
Grav_final.R | Grav results, Emissions Excel sheet and upas_summary.R | Final concentrations | 

## Slide 8: Mobenzi Specific Overview
QA/QC
  Mobenzi import function
  Flagging function
    ? Hopefully just do this manually
  Filename checking function (of the study ID)
  Automated processing/emails

## Slide 9: Code workflow for Lascars and PATS+ deployment data streams
Imports data from Dropbox, analyzes them, applies calibrations, sends summary
Code name | Inputs | Outputs | Notes
Thresholds.R | -- | Threshold values used for generating flags | See readme for details
Functions.R | Data files, calibration factors | Summary of data called upas_summary.R, calibrated real-time data files | 
localBatchScript.R | Data files; thresholds.R; functions.R | CSV file with summary of UPAS results and flags | 
HAPIN_quack.R | All above files; | CSV file with file summaries, sent to selected IRC recipients. Then used in the QAQC Excel doc | 

## Slide 10: Code workflow for modeling data streams
Code name | Inputs | Outputs | Notes
Household_chracteristics.R | Mobenzi data | Household_data | 
Household_air_pollution.R |  | Household_air_pollution | Real-time and summary HAP data.
Per_PM_exp.R |  | perp_PM_exp | Real-time and summary PE data
Area_PM_exp_processing.R |  | Area_PM_exp | 
PATS_realtime_QC.R |  | Realtime_ECM_qa | 
Field_bn.R |  | Blank_Filter | 
Beacon_system.R |  | Beacon_emitter | Proximity data time series.
Beacon_system.R |  | Beacon_logger | 
CO_exposure.R |  | CO_exp | 

## Slide 11: If errors in file names are found use the following process:
Make a copy of the file with the incorrect name (e.g. “INCORRECT FILE NAME.txt”) and name the new copy “INCORRECT FILE NAME _ FIXED_ CORRECTED NAME.txt”
  Never delete the original file
Move the original file with the incorrect name to the Dropbox folders called "Corrected Files”
The new file should remain in the original folder it was found in
Example of an incorrect file and the correction (HHID was incorrect):
  Incorrect file name: “23003_PEM_2_ECM00039_2M50408_10092018.txt”
  Make a copy and name it “23003_PEM_2_ECM00039_2M50408_10092018_FIXED_23004_PEM_2_ECM00039_2M50408_10092018.txt”
  The original file with the incorrect file name should be located in the ‘Correct File’s folder
  The correct file should be in the same place as it was originally found
Remember to change the names of all versions of files, for example, both raw and processed files for the ECMs!
Notes: Proposed workflow: Use CRF H41 to gather all relevant data for a deployment. Expected files are based on dates/user/HHIDs/device IDs.
  If expected files are not found, or only match some of the matching variables, flag the file, and allow a user to create a new file version with the correct data.