## Slide 1: Carbon Balance Method
Ryan Thompson
Department of Civil and Environmental Engineering

## Slide 2: Carbon Balance Applications
EPA Reference Method for vehicle emission factors
EPA alternate method for stack sampling
Open biomass
Brick Kilns
Cookstoves
Notes: Carbon balance search on the internet refers to the carbon in the earth system (soil, plants, ocean, atmosphere)

## Slide 3: Carbon Balance for Cookstoves
Smith, K.R. et. al., 1993. Greenhouse gases from biomass and fossil fuel stoves in developing countries: A Manila Pilot Study. Chemosphere: http://ehs.sph.berkeley.edu/krsmith/publications/Chemo-03.pdf
Zhang, J. et. al., 1999. Greenhouse gases and other airborne pollutants from household stoves in China: A database for emission factors. Atmospheric Environment: http://ehs.sph.berkeley.edu/krsmith/publications/00_zhang_1.pdf
US EPA, 2000. Greenhouse gases from small scale combustion devices in developing countries: http://ehs.sph.berkeley.edu/krsmith/publications/00_smith_3.pdf
Bertschi I.T. et. al.,2003. Trace gas emissions from the production and use of domestic biofuels in Zambia measured by open-path Fourier transform infrared spectroscopy. Journal of Geophysical Research-Atmospheres.
Roden, C., Bond, T., 2006. Emission Factors and Real-Time Optical Properties Emitted from Traditional Wood Burning Cookstoves. Environmental Science and Technology.
Roden, C. et. al., 2009. Laboratory and field investigations of particulate and carbon monoxide emissions from traditional and improved cookstoves. Atmospheric Environment.
Chen, Y. et. al., 2012. Characterizing biofuel combustion with patterns of real-time emission data (PaRTED). Environmental Science and Technology

## Slide 4: Carbon Balance Method Definition:
Carbon Mass Balance Equation
Cfuel – Cchar = CCO2 + CCO + CTHC + CPM
Where:
Cfuel mass of carbon in fuel (g)
Cchar mass of carbon in remaining char (g)
CCO2 mass of carbon in carbon dioxide (g)
CCO mass of carbon in carbon monoxide (g)
CTHC mass of carbon in total hydrocarbons (g)
CPM mass of carbon in particulate matter (g)
Balance the carbon in the emissions with the carbon in the fuel

## Slide 5
Carbon
Consumed
Carbon Mass Balance Equation
Carbon
Emitted
Cfuel – Cchar = CCO2 + CCO + CTHC + CPM

## Slide 6: Uses of the Carbon Balance Method
Total Capture Hood
  Calculate real-time burn rate
  Provide quality assurance check for the total capture method
  Alternate method to calculate total emissions
Partial Capture Field Measurements
  Calculate emission factors with limited equipment
  Calculate total emissions

## Slide 7: Total Capture Hood Carbon Balance for Real-Time Burn Rate
Emission rate = conc x flow
We can’t weigh the fuel every second but we can measure the emissions every second.

## Slide 8
Total
Capture
Carbon Balance
Total Capture Hood Carbon Balance for Real-Time Firepower
Flow
fuel
firepower
fuel

## Slide 9
Total
Capture
Carbon Balance
Total Capture Hood Carbon Balance for Real-Time Firepower

## Slide 10: Total Capture Hood Carbon Balance for Quality Assurance
Total emission = conc x flow x time
compare

## Slide 11: Total Capture Hood Carbon Balance for Quality Assurance
compare
Total
Capture
Carbon Balance
Carbon consumed
total emissions
flow
carbon emitted
Scale
time
Fuel carbon
fraction
Char carbon
fraction

## Slide 12: Total Capture Hood Carbon Balance for Quality Assurance
Hood carbon balance
= percentage of emissions that were captured
WBT v5
Aprovecho v4.2.2

## Slide 13: Total Capture Hood Carbon Balance for Quality Assurance
Scale
Total
Capture

## Slide 14
Measured inputs:
, CO2 concentration
, CO concentration
PM concentration
Duct pressure
Duct Temperature
Duct volumetric flow rate
Sample time
Carbon fraction of PM
, Fuel mass
Carbon fraction of fuel
, Char mass
Carbon fraction of char
Moisture content (wet basis)
Total Capture Hood Carbon Balance for Quality Assurance

## Slide 15
Uncertainties to consider:
, CO2 concentration
, CO concentration
Duct volumetric flow rate
Carbon fraction of fuel
, Char mass
Carbon fraction of char
Moisture content (wet basis)
If the carbon doesn’t balance…
Total Capture Hood Carbon Balance for Quality Assurance

## Slide 16: 100% CO2 Injection
Total Capture Hood Carbon Balance for Quality Assurance

## Slide 17: Partial Capture Carbon Balance Emission Factors

## Slide 18: Partial Capture Carbon Balance Total Emissions
Calculate total emissions without collecting the total emissions

## Slide 19: Partial Capture Carbon Balance
weigh fuel
carbon
fraction
Ideal gas law
PM
molecular weight
carbon
fraction
Notes: Don’t know know much

## Slide 20: Partial Capture Carbon Balance
Scale
Emission
Factors
Total
Emissions

## Slide 22: Partial Capture Carbon Balance
Advantages
  Calculate emission factors with small sample probe
  Calculate total emissions without collecting total emissions
  No flow measurement required – more appropriate if uncertain flows
  Unaffected by dilution
  Allows field measurements with portable, cheap equipment
  Opens a new frontier of emission sampling
  Makes emission sampling accessible to more people
Disadvantages
  Requires good understanding of the fuel, such as the carbon fraction.

## Slide 23: Lab Tests: Total Capture or Partial Capture?
Measure flow
Measure flow
Measure fuel
Measure emissions ratio
Know fuel carbon fraction.
Measure fuel

## Slide 24: Conclusion
The carbon balance is useful in the lab
  to measure real time fuel consumption, firepower, and emission factors
  Check total capture emission measurements
  Calculate total emissions
The carbon balance allows field measurements of emission factors and total emissions with portable equipment

## Slide 25: Thanks
Jim Jetter, US EPA
Tami Bond, Cheryl Weyant, University of lllinois